|  |  | Maximum Flame 5 psi oxygen ¼ psi propane |
| --- | --- | --- |
| Bobcat | Candle length: Flame width: Flame length: Oxygen consumption: Propane consumption: | 0.60” 0.75” 13” 12 CFH 3 CFH |
| Minor | Candle length: Flame width: Flame length: Oxygen consumption: Propane consumption: | 0.40” 0.75” 11” 11 CFH 2 CFH |
| Mini CC | Candle length: Flame width: Flame length: Oxygen consumption: Propane consumption: | 0.30” 0.50” 7” 12 CFH ~ 2 CFH (slightly less than 2) |

|  |  | Neutral flame 3/8” candles 8 psi oxygen 2 psi propane | Maximum boro flame 8 psi oxygen 2 psi propane |
| --- | --- | --- | --- |
| Bobcat | Candle length: Flame width: Flame length: Oxygen consumption: Propane consumption: | 0.375” 0.75” 11” 6 CFH 1 CFH | 1.5625” 1” 16” 16 CFH 6 CFH |
| Minor | Candle length: Flame width: Flame length: Oxygen consumption: Propane consumption: | 0.375” 0.75” 11” 9 CFH 2 CFH | 1.25” 1” 12” 16 CFH 5 CFH |
| Mini CC | Candle length: Flame width: Flame length: Oxygen consumption: Propane consumption: | 0.375” 0.75” 11” 14 CFH 2 CFH | .65” .80” 12” 20 CFH 5 CFH |